## Slide 1: AC-Key: Adaptive Caching for LSM-based Key-Value Stores
Fenggang Wu, Ming-Hong Yang, Baoquan Zhang, and David H.C. Du
ATC ‘20
Presenter: Kai Li

## Slide 2: Background
In enterprise workloads, read operations exhibit “hot spots” in LSM-tree-based KVSs (LSM-KVS) for both point lookups and range queries.
Caching “hot spots” can improve read performance.
Three type of entries that can be cached in LSM-KVS: Block, Key-Value (KV), and Key-Pointer (KP).

## Slide 3: Motivation
Caching LSM-KVS is challenging
  Data have different sizes/levels -> different cache costs/benefits
    Cache a record at a deeper level can bring more benefits, as it reduces more storage IOs
  Different type of read: point lookup, range query
    Cache a block favors range query
    Cache a KV/KP favors point query
    When value size is large
      Cache a KP is more space-efficient than cache a KV
Existing caching schemes are not effective
  Only consider one or two types of entries to cache among KV, KP, and block
  Fixed allocated cache size for one type of entry
  Not efficient for dynamic workloads
Source: https://www.usenix.org/system/files/atc20-paper107-slides-wu.pdf

## Slide 4: Cache Size Adjustment with Ghost Cache
Adaptive Replacement Cache (ARC)
  Real Cache + Ghost Cache
  Ghost Cache hit will push the
  boundary
  Adaptive to different cache components

## Slide 5: AC-Key: Hierarchical Adaptive Caching
Upper Level: Point Cache vs Block Cache
Lower level: KV Cache vs KP cache

## Slide 6: Get Handling
Case I: Hit in KV Cache
  The value is returned without any I/O incurred.
Case II: Miss in KV Cache but hit in KP Cache.
  Check Block Cache (and bring to Block Cache if missing)
  Promote KP Cache to KV Cache
Case III: Miss both in KV Cache and KP Cache.
  Search every sorted run level by level
  Move into KP Cache

## Slide 7: Flush and Compaction
Sync the caches only in flushing time, not during Put
AC-Key updates KP and block Caches when compaction affects any of cached KP entries or blocks

## Slide 8: Caching Efficiency Factor
To quantitively analyze the trade-off between the costs and benefits of the cache entries
  Target Boundary Adjustment by Caching Efficiency Factor E
  Adjustment ∆ = kE

## Slide 9: Evaluation
Implementation on RocksDB, 5.6K LoC.
Compare AC-Key with pure-kv, pure-kp, rocksdb, offline

## Slide 10: Extensive Evaluations

## Slide 11: Thank you! Q&A